2016 - Formulae Sheet

I= 0.5CEN

Ea	  =  Self absorption factor (%/100)

Ec	  =  Instrument Counting Efficiency (%/100)

Ef	  =  Fractional collection efficiency (%/100)

F	  =  Air flow rate through the filter (ft3/min)

Rb	  =  Background count rate (cpm)

Rg	  =  Gross count rate (cpm)						          Confidence Level (CL)

Rn	  =  Net count rate (cpm)							50% 	-	 0.6745

Ng	  =  Gross number of counts measured during gross count time (Tg)		68% 	- 	1.0000

Tb	  =  Background count time (min)						90% 	- 	1.6449

Tg	  =  Gross sample count time (min)						95% 	- 	1.9600

Ts	  =  Duration of air sample collection (min)					99% 	-	2.5750

6.29E10 =  Conversion Constant (dpm*ml/uCi*ft3)					99.7	-	3.0000

k		=  1.6E-11 (conversion factor [uCi*ft3]/[ dpm*ml]

Eberline RO-20 Contact and 1/8 inch Correction Factors for Disc Sources

| Disc Diameter, cm (in.) | Correction Factor for Contact Measurements |
| --- | --- |
|  | For exposure rate on contact with source | For exposure rate at 3mm (1/8 in.) from source |
|  | Beta (a, b) | Gamma (a, c) | Beta (b) |
| 1.27 (0.5) | 250 | 54 | 180 |
| 2.54 (1.0) | 46 | 26 | 55 |
| 5.08 (2.0) | 15 | 8 | 13 |
| 7.62 (3.0) | 6 | 5 | 6 |
| NOTEd - When making measurements where the meter is ≥ 2.54 cm (≥ 1 in.) away from the source and for beams ≥ 7.62 cm. (≥ 3 in.), the general correction factors below are used: • 2 for window-open beta readings • 1 for window-closed gamma readings a. Measured with source surface on contact with the beta shield guide rails. b. Non-penetrating radiation correction factors based on 204Tl (Beta Max = 0.763 MeV). c. Penetrating radiation correction factors are based on 137Cs, source in contact with the beta shield. d. Field geometry correction factors can be applied to objects with a smallest dimension > 18 in., provided that dose rates are uniform across the surface. |